Sample Preparation
mechanically / physically remove visible extraneous material or select material of interest
bulk soil/sediment:
rinse sample through the 0.14 mm sieve using UPW,
gently pestle in the sieve as needed to aid disaggregation
add UPW to raise volume to 25-50 mL
add 25-35 mg aluminum sulfate
gently agitate to dissolve and disperse aluminum sulfate
centrifuge 2 minutes
if supernatant remains cloudy,
add an additional 25-35 mg aluminum sulfate, agitate and centrifuge again.
decant supernatant
transfer selected material to 50 mL centrifuge tube
if sample is wet, dry on heat block under foil tent @ 25..60 °C
bulk soil/sediment:
de-select as much fine, light-colored sediment from bottom as possible
pestle top crust through sieve to < 2 mm chips
de-select < 0.3 mm fraction if available sample mass permits
weigh sample, record mass

ABA - acid, base, acid
(Do not rinse between base and acid washes. After each step, centrifuge if necessary to concentrate sample, and decant or pipette and discard supernatant unless otherwise noted.)

acid wash: immerse ≥ 30 minutes in 5..10 mL 1 N HCl @ 60 °C
(use more solution if sample is large)

base wash: immerse ≥ 1 h in 30..40 mL 1 N NaOH @ 60 °C
repeat until supernatant is colorless or color stops fading on successive washes
if supernatant is very dark after centrifuging, do not discard it; instead
transfer supernatant to a second 50 mL centrifuge tube,
marked with the sample ID plus "B" (for Base-soluble fraction)
add 10 mL 6 N HCl to the B fraction, cap tube and swirl to combine reagents
allow 5..10 minutes for humic acids to begin coalescing and settling
centrifuge to concentrate B fraction
decant and discard B fraction supernatant (it is normally yellowish)
collect, precipitate and concentrate subsequent base step supernatants, also
combine each one into this same B-fraction tube
stop collecting B-fraction supernatants
when they become transparent light brown or yellow in color

acid wash: immerse ≥ 10 minutes in 5..10 mL 1 N HCl @ 60 °C

rinse: immerse ≥ 1 minutes in ≥ 40 mL UPW @ 25..60 °C
bulk soil/sediment: if the supernatant is cloudy after centrifuging a rinse step
add 25-35 mg aluminum sulfate
gently agitate to dissolve and disperse aluminum sulfate throughout the supernatant
avoid involving already-consolidated material
centrifuge 2 minutes
if supernatant remains cloudy,
add an additional 25-35 mg aluminum sulfate, agitate and centrifuge again
decant supernatant
repeat until pH ≥ 4

dry in vacuum oven or in heat block under foil tent @ 25..60 °C

bulk soil/sediment:
de-select as much fine, light-colored sediment from bottom as possible
pestle top crust through sieve to < 2 mm chips
de-select < 0.3 mm fraction if available sample mass permits

if B-fraction was collected,
dry B-fraction thoroughly in heat block under foil tent @ 60 °C
add ≥ 40 mL pH3 water, cap tightly and shake vigorously for several seconds
(This dissolves salt and dislodges most of the solids from the tube wall.)
centrifuge; decant and pipette to discard as much supernatant as possible
(repeat, if desired, to further improve B-fraction weight accuracy.)
dry in heat block under foil tent @ 60 °C
weigh dried B-fraction, record mass

weigh sample, record mass