Reagent preparation
chromic acid solution is (0.1 M K2Cr2O7 in 2 M H2SO4)

Implement Preparation

Vials, pipette tips, glass, mortar and pestle
clean in sub-boiling chromic acid for at least 2 h
rinse 3 times
store in sealed container for later use

Metal implements, including forceps and spatulas
sonicate 1 h in Alconox (9 g / gal).
rinse 3 times
sonicate 1 h in UPW
rinse 3 times
sonicate 1 h in UPW

Sample Preparation
select 15..25 mg of sample material (charcoal or graphite only)
transfer to 50 mL centrifuge vial
add 1 drop of UPW to vial and crush with pre-cleaned glass rod
rinse
crush sample to powder < 1 mm with mortar and pestle

if silicates are to be removed in addition to carbonates
immerse 8..16 h in 5-10 mL of 1:1 (28 N HF : 12 N HCl) @ 60 °C
otherwise, remove carbonates:
immerse 30 m in 5-10 mL of 1 N HCl @ 60 °C

remove humic acids and other base-soluble organic compounds
immerse 1 h in 30 mL of 1 N NaOH @ 60 °C
centrifuge and decant or pipette and discard supernatent
repeat until supernatent is clear

remove non-elemental carbon compounds
immerse 14..24 h in 30 mL of chromic acid @ 60 °C
rinse 5 m in 40 mL UPW @ 60 °C
repeat until rinse water is clear and 4 < pH < 7

centrifuge if needed and decant or pipette and discard supernatent
leave sample entirely at bottom of centrifuge vial (not on the sides)
dry in vacuum oven or on heat block under foil tent at 60..80 °C
(usually requires 1..2 h)

Waste disposal
treat waste chromic acid to convert hexavalent chromium to trivalent