Sample Preparation
Woody, reedy, paper, skin, parchment, and leather samples may benefit from this treatment.
mechanically / physically remove visible extraneous material
remove sediments and other macro-contaminants; sonicate in UPW if needed
pulverize or shave to < 2 mm thick slices
transfer to new 50 mL centrifuge vial
if wet, dry on heat block under foil tent @ 60 °C
weigh sample, record mass
select test sample of up to 40 mg

BABAB - base, acid, base, acid bleach
(After each step, centrifuge if needed to concentrate sample, then decant or pipette to remove and discard supernatant.)

Preliminary strong base step
optional; may be omitted unless desired to ease maceration of sample to fibers
8..16 h in 5 N NaOH @ 60 °C
crush to fibers, ensure thorough maceration; leave no floating pieces

Perform standard ABA protocol for organic samples
optional: terminate ABA after base washes and continue with bleach step below

Bleach
optional: replace the final acid step of ABA with this step
bleach 0.5 .. 16 h in 5-10 mL solution @ 60 °C (loosely covered, in fume hood)
solution if replacing ABA final acid step
equal parts 1 M NaClO2 and 1 N HCl
solution if performed after ABA final rinses
equal parts 1 M NaClO2 and pH3 water (0.001 N HCl)
monitor color of solution, color of sample material and amount of sample
disappearance of gold color of solution indicates ClO2 is exhausted
bleach again in fresh solution
continue bleaching until the product (holocellulose) is white
or the sample appears to be suffering excessive losses
soak 30 m in 40 mL UPW @ 60 °C

alpha-cellulose concentration (optional; skip if sample loss must be avoided)
1 h in 6 mL 5 N NaOH @ room temperature
30 m in 6 mL 6 N HCl @ 60 °C

wash 5 m in UPW @ ≤ 60 °C (repeat until pH > 4)
dry in vacuum oven @ ≤ 60 °C, or on heat block under foil tent @ 60 °C
weigh sample, record mass and cellulose yield