Convert hexavalent chromium to trivalent chromium

Observe the amount of chromic acid waste to be treated. If there is a large quantity, then treat it in multiple smaller batches, each no more than 3/4 the volume of the largest available beaker (1/5 the volume if the chromic acid waste is concentrated).

Dilute the waste
This step may be omitted if the chromic acid waste is already diluted by half or more (e.g., when it is diluted by rinsing after use, or when the initial solution was prepared with a greater volume of water than sulfuric acid.) Use a clean beaker of at least 5 times the volume of the concentrated chromic acid waste to be treated. Pour an equal volume of water into the empty beaker, then slowly add the chromic acid waste to the water.

Put a stir bar into the beaker, place the beaker on a magnetic stirrer and turn it on.

Check the pH of the mixture. If the pH is less than 1, gradually add small amounts of sodium carbonate (Na2CO3, "soda ash" or "washing soda") to the pH of the mixture to 1.

Slowly add small amounts of sodium thiosulfate (Na2S2O3, "hypo") until the solution becomes blue and cloudy. Pre-crushing the Na2S2O3 crystals speeds dissolution. Wait for added crystals to completely dissolve before adding more. From pure chromic acid, the appearance transitions from bright orange through dull orange, green, bluish green, more blue, and finally it will start to become cloudy. Other dissolved substances in the waste may affect the colors somewhat. The reaction can produce some sulfur-smelling gas; use a fume hood if necessary.

Add sodium carbonate (Na2CO3) to neutralize the solution (6 < pH < 8). If too much Na2CO3 is added and the solution becomes basic, add HCl to neutralize it. Cover the beaker with a watch glass whenever the solution effervesces.

Once the solution is neutral, continue stirring for 15 minutes.

The (safe) trivalent chromium compounds will precipitate out of the solution. This typically takes 30 minutes or more. The supernatant is safe for sewer or landfill. It may be decanted and poured down the drain, discarded into the trash, or evaporated away. The precipitate is safe for landfill. Discard it into the trash. If desired, centrifuge to concentrate the precipitate, and/or evaporate to dryness before discarding.

Notes
Dichromic acid (H2Cr2O7) is probably also present in chromic acid, along with the mixed chromic-sulfuric acid (H2CrSO7). (Wikipedia)

From "1997 Armenante - Precipitation of Heavy Metals from Industrial Wastewaters.pdf"

Chromium is typically precipitated in two steps:
hexavalent chromium (Cr+6) is reduced to trivalent chromium (Cr+3). Compounds such as FeSO4, Na2S2O5 (sodium bisulfite) or SO2 (sulfur dioxide) are used as reducing agents. The reaction is conducted at low pH (< 3)

trivalent chromium is precipitated as Cr(OH)3. Lime is typically used for the precipitation reaction. The effluent concentration is 0.2 ppm at pH 7.5

The reactions involved in chromium precipitation are:
Reduction reaction (at pH < 3):

H2Cr2O7 + 3SO2 → Cr2(SO4)3 + H2O

(i.e., 1.85 ppm SO2/ppm Cr) or, alternatively:

H2Cr2O7 + 6FeSO4 + H2SO4 → Cr2(SO4)3 + 3Fe2(SO4)3 + 7H2O

Precipitation reaction (at pH of 8 to 9):

Cr2(SO4)3 + 3Ca(OH)2 → 2Cr(OH)3 ↓ + 3CaSO4

(i.e., 2.13 ppm Ca(OH)2/ppm Cr)
(what does the down arrow mean?)

(From Chromium(VI) Handbook, eds Guertin et al., about Cr(VI) dissolved in groundwater.) In the thiosulfate (S2O32-) reaction, the S atom is converted from a +2 oxidation state to a +2½ oxidation state when S2O32- reacts to form the tetrathionate anion (S4O62-). One mole of electrons are released for each mole of S2O32- that is consumed during the reaction.
The redox reaction shows that 3 moles of Na2S2O3 are required to reduce 1 mole of Cr(VI). This is equivalent to 9.12 mg/L Na2S2O3 to reduce 1 mg/L of Cr(VI) dissolved in groundwater.

Reduction: 8H+ + CrO42- + 3e- → Cr3+ + 4H2O
Oxidation: 6S2O32- → 3S4O62- + 6e-
16H+ + 2Cr2O42- + 6S2O32- → 2Cr3+ + 3S4O62- + 8H2O

reactants:

?H+ + K2Cr2O7 + 7H2SO4 + Na2S2O3 + ?e-

  →

possible products:
Cr2(SO4)3
 K2SO4
 7H2O
Cr(OH)3
 H2O

14H+ + Cr2O72- + 6S2O32- → 2Cr2+ + 3S4O62- + 7H2O

 K2Cr2O7 + H2O → 2K+ + 2H+ + 2CrO42-

(dichromate is an anhydride of chromate)

Chromate: CrO42-(aq) (yellow)
Dichromate: Cr2O7-(aq) (orange)

In aqueous solution, chromate and dichromate anions exist in chemical equilibrium:

 2CrO42- + 2H+ ↔ Cr2O72- + H2O(l)

 CrO42-(aq) + 2H3O+(aq) ↔ Cr2O7-(aq) + 3H2O(l)

When used as oxidizing agents (or titrants) in a redox chemical reaction, chromates and dichromates convert into trivalent chromium, Cr3+, salts of which typically have a distinctively different blue-green color

Chromate and dichromate ions are fairly strong oxidizing agents. Commonly three electrons are added to a chromium atom, reducing it to oxidation state +3. In acid solution the aquated Cr3+ ion is produced.
Cr2O72− + 14 H3O+ + 6 e− → 2 Cr3+ + 21 H2O (ε0 = 1.33 V)
In alkaline solution chromium(III) hydroxide is produced. The redox potential shows that chromates are weaker oxidizing agent in alkaline solution than in acid solution.[5]
CrO42- + 4 H2O + 3 -
e → Cr(OH)3 + 5 OH− (ε0 = −0.13 V)

(From 2003 Armaitis et al - Calculation of Limiting Diffusion Currents in Cr(VI) Solutions, Protection of Metals, Vol 39, Number 2, 124-132) In Cr(VI) solutions, a number of chromium-containing anions are present simultaneously. Their reduction proceeds according to the summary cathodic reaction:
H2 - zCrnO3n + 1z- + (6n + z - nq)H+ + 3ne- → nCr(OH)q(3 - q)+ + (3n + 1 - nq)H2O

In redox processes, the reductant transfers electrons to the oxidant. Thus, in the reaction, the reductant or reducing agent loses electrons and is oxidized, and the oxidant or oxidizing agent gains electrons and is reduced. The pair of an oxidizing and reducing agent that are involved in a particular reaction is called a redox pair. A redox couple is a reducing species and its corresponding oxidized form, e.g., Fe2+/Fe3+.

Oxidation
reductant → products + ne-
(reductant is oxidized; it loses electrons; its oxidation number increases)

Reduction
 oxidant + ne- → products
(oxidant is reduced; it gains electrons; its oxidation number decreases)

16H+ + 2Cr2O42- + 6S2O32- → 2Cr3+ + 3S4O62- + 8H2O

14H+ + Cr2O72- + 6S2O32- → 2Cr2+ + 3S4O62- + 7H2O