load material into quartz boat and load boat into center of tube furnace
close O2 valve

start vacuum system

rough, then evacuate bake-out tube (open BOT-VM)
plug in fans
set “Percent Time On” to HI
start “warm-up” timer
11 minutes for borosilicate glass (Pyrex, Kimax, etc)
20 minutes for quartz
wait for timer

set “Percent Time On” to:
1.8 for pyrex (approx 600 °C true, 500 °C indicated)
4.9 for quartz (approx 900 °C true, 800 °C indicated)

wait until furnace reaches temp
500 °C indicated for pyrex
800 °C indicated for quartz

close BOT-VM (isolate bake-out tube)
introduce 200-300 Torr O2, then close O2 valve
start 2 hour timer
wait for timer

turn off tube furnace
rough, then evacuate bake-out tube (open BOT-VM)
wait for furnace to reach room temperature

close BOT-VM (isolate bake-out tube)
shut down vacuum system

unload tube (do not touch baked-out glass with bare hands)
store baked-out glass in desiccator