General rules
Never touch glassware (tubes, beads, etc) with gloved hands.
Never touch anything that goes inside the combustion tube; always pour or use forceps.
Blow out all test tubes and vials with compressed N2 or dry, filtered air before loading.

GR materials
Fe: 2.50 to 2.75 mg into 6 mm x 50 mm borosilicate tube
Mg perchlorate: ~30 mg, ~6..8 mm, into 6 mm x 50 mm borosilicate tube

immediately cover each loaded tube with foil
Fe tubes may be prepared in advance
perchlorate tubes must be prepared just before use

Organic samples (for 850 to 950 μgC)
oxalic acid (Ox1, Ox2, C7, C8), 19.05 %C: 4.5 to 5.0 mg (2x: 8.9 to 10.0; 3x: 13.4 to 15.0)
AAG, CG: 0.85 to 0.95 mg
charcoal: 1.4 to 2.4 mg
collagen: 2.1 to 2.4
cellulose: 2.1 to 2.7
wood, seed, plant matter: 2.1 to 3.6 mg
peat: 2 to 20 mg
soil, sediment: 20 to 150 mg
humic acids (“B fractions”): 2 to 3 mg

load appropriate quantity of sample into 6 mm x 25 mm quartz sample tube ("durham tube")
insert sample tube open end first into horizontal 9 mm quartz combustion tube
turn combustion tube upright to drop the sample tube and sample to bottom
fill combustion tube with quartz beads and sugar according to template
mark the loaded combustion tube with sample ID & mass (in micrograms)

Carbonate samples (for 850 to 950 μgC)
C1, C2, shells, limestone, etc: 7.7 to 9.5 mg	(2x: 17.0 to 19.0; 3x: 25.5 to 28.5)

load pretreated carbonate sample material into Exetainer vial
mark vial with sample ID & mass (in micrograms)
cap vial with septum cap and perform "Prepare carbonate sample for acid" procedure
mark cap to indicate sample is ready for acid digestion